## Slide 1: BSW – BASIC SOFTWARE
BSW
DCOM
COM
EM
Microcontroller
Basic Software
Runtime Environment (RTE)
Application Layer
DCOM
COM
EM

## Slide 2: BSW – BASIC SOFTWARE
NRC | Description
12 | Sub-function is not supported
13 | Incorrect message length or invalid format
78 | Request correctly but response pending
7E | Sub-function is not supported in active diag sessions
33 | Occuring when we haven’t unlocked the security access
7F | When we send service 2E in unsupported session
31 | When we send service 2E with invalid DID or we send service 28 with invalid communication type
22 | When the conditions aren’t correct
24 | Request sequence error
35 | Invalid key
36 | Exceed Number of Attempts. Most of the OEMs will not allow to send wrong key more than 3 times
37 | Required time delay not expired
Addressing | Description
Physical addressing | Static address of ECU’s
Functional addressing | 
Sub –function | Description
00 | Use only in tester present mode (Service 3E)
01 | Default session
02 | Programing session
03 | Extended session
Terms | Description
DID | Diagnostic Identifier
VIN | Vehicle Identification
DTC | Diagnostic Trouble Code
BSW
DCOM
COM
EM

## Slide 3: DCOM
SERVICE | DESCRIPTION
10 | Change Sessions
3E | Tester present
2E | Write DID (Diagnostic Identified)
22 | Read DID
19 | Read DTC (Diagnostic Trouble Code)
14 | Clear DTC
85 | Control DTC
11 | Reset ECU
27 | Security Algorithm
28 | Communication Control
BSW
DCOM
COM
EM

## Slide 4: SERVICE 10 – Change Sessions
DCOM
SERVICE 3E
SERVICE 2E
SERVICE 22
SERVICE 19
SERVICE 14
SERVICE 85
SERVICE 11
SERVICE 27
SERVICE 28
PROG
SESSION
DEFAULT
SESSION
EXT
SESSION
5s-10s
5s-10s
SO SHORTLY TIME !!!
TESTER
PRESENT
To keep long time !!!
SERVICE 3E
Normally
10 02
ECU
Application mode
BootLoader mode
BootLoader
Wait a few time to BootLoader active
Application mode
SERVICE 10

## Slide 5: SERVICE 10 – Change Sessions
Sub-function | Request | Response
01 | 10 01 | 50 01 xx xx xx xx
02 | 10 02 | 50 02 xx xx xx xx
03 | 10 03 | 50 03 xx xx xx xx
Supported NRC | Example
12 | 10 08 -> 7F 10 12
13 | 10 01 03 -> 7F 10 13
78 | 10 02 -> 7F 10 78, because It takes a few time to active bootloader, we need wait about 100-500ms
7E | … -> 7F 10 7E
DCOM
SERVICE 3E
SERVICE 2E
SERVICE 22
SERVICE 19
SERVICE 14
SERVICE 85
SERVICE 11
SERVICE 27
SERVICE 28
SERVICE 10

## Slide 6: SERVICE 3E – Tester Presents
OTHER SESSIONS
DEFAULT SESSION
Keep long time…
ECU
TESTER
Tools
Panel
3E 00
7E 00
NRC supported | Example
12 | 3E 01 -> 7F 3E 12
13 | 3E 00 03 -> 7F 3E 13
Only supported sub-function 00
Supported Addressing
Physical Addressing
Functional Addressing
DCOM
SERVICE 3E
SERVICE 2E
SERVICE 22
SERVICE 19
SERVICE 14
SERVICE 85
SERVICE 11
SERVICE 27
SERVICE 28
SERVICE 10

## Slide 7: SERVICE 2E – Write DID
Supported Addressing
Physical Addressing
TESTER
ECU
2E F1 90 [DID data]
6E F1 90
F1 90
VIN – Vehicle Identification
START
Change to Ext Session
Unlock Security
OEM’s
Avoid any one can write wrong information to ECU
Be setted security
Need Unlock security before write DID
Write DID
Supported NRC | Example
31 | 2E AB CD -> 7F 2E 31
13 | 2E F1 90 -> 7F 2E 13
33 | … -> 7F 2E 33
7F | … -> 7F 2E 7F
DCOM
SERVICE 3E
SERVICE 2E
SERVICE 22
SERVICE 19
SERVICE 14
SERVICE 85
SERVICE 11
SERVICE 27
SERVICE 28
SERVICE 10

## Slide 8: SERVICE 22 – Read DID
Description | Request | Sample Response
Network information data identifier | 22 F1 20 | 62 F1 20 [4 bytes data]
Function specification data identifier | 22 F1 21 | 62 F1 21 [4 bytes data]
SW Version Number data Identifier | 22 F1 89 | 62 F1 89 [4 bytes data]
HW Version Number data Identifier | 22 F0 89 | 62 F0 89 [4 bytes data]
VIN data Identifier | 22 F1 90 | 62 F1 90 [17 bytes data]
ECU Serial number data Identifier | 22 F1 8C | 62 F1 8C [13 bytes data]
Supported NRC | Example
13 | 22 F1 -> 7F 22 13
31 | 22 AB CD -> 7F 22 31
33 | … -> 7F 22 33
Supported Addressing
Physical Addressing (MAINLY)
Functional Addressing
DCOM
SERVICE 3E
SERVICE 2E
SERVICE 22
SERVICE 19
SERVICE 14
SERVICE 85
SERVICE 11
SERVICE 27
SERVICE 28
SERVICE 10

## Slide 9: SERVICE 19 – Read DTC
DCOM
SERVICE 3E
SERVICE 2E
SERVICE 22
SERVICE 19
SERVICE 14
SERVICE 85
SERVICE 11
SERVICE 27
SERVICE 28
SERVICE 10
Sub-functions | Description
01 | Number of active DTC
02 | Actual DTC (active/passive)
04 | DTC snapshot data
06 | DTC extended data
0A | All the DTC in the ECU
Request | Response
19 01 09 | 59 01 [2 bytes number of DTC]
19 02 09 | 59 02 [3 byte DTC] 09
19 04 --- | Be supported base on specific project
19 06 --- | Be supported base on specific project
19 0A 09 | 59 0A [List of all supported DTC] 09
Supported NRC | Example
13 | 19 01 09 00 -> 7F 19 13
12 | 19 0E 09 -> 7F 19 12
31 | 19 04 C1 29 87 01 -> 7F 28 31 (DTC: C1 29 87 is not supported)
78 | 19 01 09 -> 7F 19 78, because it takes a few time to active bootloader, we need wait about 100-500ms

## Slide 10: SERVICE 14 – Clear DTC
TESTER
14 FF FF FF
(Make sure 4 bytes)
54
ECU
MCU
EEPROM
Contain DTC’s
Send clear signal
FF FF FF
DTC’s Group
Supported NRC | Example
13 | 14 FF FF -> 7F 14 13
31 | 14 00 00 00 -> 7F 14 31
DCOM
SERVICE 3E
SERVICE 2E
SERVICE 22
SERVICE 19
SERVICE 14
SERVICE 85
SERVICE 11
SERVICE 27
SERVICE 28
SERVICE 10

## Slide 11: SERVICE 85 – Control DTC
DTC Setting
DTC Status mask
DTC Status Mask | 
0 | Test fail
1 | Test fail this operation cycle
2 | Pending DTC
3 | Confirmed DTC
4 | Test not completed since last clear
5 | Test failed since last clear
6 | Test not completed this operation cycle
7 | Warning indicator logic
09 |  |  |  |  |  |  | 
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
08 |  |  |  |  |  |  | 
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
01 |  |  |  |  |  |  | 
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
DCOM
SERVICE 3E
SERVICE 2E
SERVICE 22
SERVICE 19
SERVICE 14
SERVICE 85
SERVICE 11
SERVICE 27
SERVICE 28
SERVICE 10

## Slide 12: SERVICE 85 – Control DTC
DTC Setting
DTC Status mask
Sub -function | Description
01 | Start DTC Setting
02 | Stop DTC Setting
Sample Request Testcase | Response | Description
85 02 | C5 02 | Stop DTC setting
timeout | - | Make a fault
19 02 09 | 59 02 [DTC data] 01 | DTC setting is stopped, so DTC confirm bit is set low level. DTC test fault bit is set high level because of fault.
85 01 | C5 01 | Start DTC setting
19 02 09 | 59 02 [DTC data] 09 | DTC setting is started, so DTC confirm bit is set high level. DTC test fault bit is set high level because of fault.
DCOM
SERVICE 3E
SERVICE 2E
SERVICE 22
SERVICE 19
SERVICE 14
SERVICE 85
SERVICE 11
SERVICE 27
SERVICE 28
SERVICE 10

## Slide 13: SERVICE 11 – Reset ECU
Sub-function | Description | Request | Response
01 | Hard reset | 11 01 | 51 01
02 | Key off on reset | 11 02 | 51 02
03 | Soft reset | 11 03 | 51 03
Modes | Detail description
Hard reset | Power-on/Start-up after the server has been previously disconnected from its power supply.
Key off on reset | When driver turns the ignition key off and back on.
Soft reset | The soft-reset value causes the server to immediately restart the application program if applicable.
Supported NRC | Example
13 | 11 01 00 -> 7F 11 13
12 | 11 00 -> 7F 11 12
33 | … -> 7F 11 33
22 | … -> 7F 11 22
DCOM
SERVICE 3E
SERVICE 2E
SERVICE 22
SERVICE 19
SERVICE 14
SERVICE 85
SERVICE 11
SERVICE 27
SERVICE 28
SERVICE 10

## Slide 14: SERVICE 27 – Security Algorithm
DCOM
SERVICE 3E
SERVICE 2E
SERVICE 22
SERVICE 19
SERVICE 14
SERVICE 85
SERVICE 11
SERVICE 27
SERVICE 28
SERVICE 10
TESTER
ECU
Request a seed [4 bytes]
Response a seed [4 bytes]
ECU
Send Key1 for compare
Key1
Use formula
Seed
Formula
Key2
Key1
Compare
same
not same
OK
NRC 35
Response this message
FORMULA
Key = [4 bytes of seed] + 00 00 4E 87
Request | Response
27 01 | 67 01 XX XX XX XX
Key [ YY YY YY YY ]= XX XX XX XX + 00 00 4E 87 | 
27 02 YY YY YY YY | 67 02
Supported NRC | Example
13 | 27 01 00 -> 7F 27 13
12 | 27 02 -> 7F 27 12
24 | … -> 7F 27 24
35 | 27 02 ZZ ZZ ZZ ZZ -> 7F 27 35
36 | … -> 7F 27 36
37 | After 3 wrong attemps, the ECU will response NRC 36, we need wait about 10min or 10 sec based on OEMs to send 27 01 again. If we don’t comply with this rule, we will receice 7F 27 37 (NRC 37)
1
2
3
3
4
5
6

## Slide 15: SERVICE 28 – Communication Control
DCOM
SERVICE 3E
SERVICE 2E
SERVICE 22
SERVICE 19
SERVICE 14
SERVICE 85
SERVICE 11
SERVICE 27
SERVICE 28
SERVICE 10
MESSAGE FORMAT [3 BYTES] |  | 
28 | XX | YY
Service | Sub-function | Communication type
Sub-functions | Enable TX | Disable TX
Enable RX | 00 | 01
Disable RX | 02 | 03
Com type | Description
01 | Normal communication message
02 | Network management communication message
03 | 01 + 03
TESTER
ECU
28 XX YY
68 XX
Supported NRC | Example
13 | 28 03 01 00 -> 7F 28 13
12 | 28 04 -> 7F 28 12
31 | 28 03 00 -> 7F 28 31
7F | … -> 7F 28 7F

## Slide 16
BSW
DCOM
COM
EM
1. Start “Trace32 Start” tool.
2. Chose “Flash” tool and select flash file.
3. Check system power status
3.1. In case power down, check power supply then chose attach
3.2. After entering running mode Flash all binaries
4. All complete, check Rx, Tx signals in coresi
COM
Flash software

## Slide 17
BSW
DCOM
COM
EM
Dataset:
Intrinsic Calibration: message use at RBEOL mode UDS format [3d][22][data] = [service function][sub-function][data]
Vehicle Variant: select variants
Static Calibration: used before enabling SUMO, TRAMO messages – need screen for calibration
*NOTE:
- UDS: Unified Diagnostic Services. A standard for Diagnostics according to ISO14229-1
COM
Configuration for Calibration (1/3)

## Slide 18
BSW
DCOM
COM
EM
1
2
4
3
Click “Activate Plant Mode”
Chose “RB EOL“mode
Check wherther Direct Rx have value and Status is “OK”
Enter the EnvDirectSend gotten from the released email then Click “Transmit”. Transmit success: “OK! Positive response”
Click Clear Idle mode Direct Rx end with “78” (Pending)
5
COM
Configuration for Calibration (2/3)

## Slide 19
BSW
DCOM
COM
EM
EnvDirectSend (Physical request)
Basic sections:
- Using service 10 (section control) for changing sections
- Sub-function:
01: Default section
02: Programing section
03: Extending section.
Direct Rx (respond from MPC)
COM
Configuration for Calibration (3/3)

## Slide 20
BSW
DCOM
COM
EM
Define MPC node
Folder structure
COM
Common xml modification
Correct the title for project name export in report file
SFCAN files
ECAN files
NOTE:
*VID_Status2.can has different testWaitForTimeout get signal
Please refer VID cycle time in DBC file for more detail.
Automation test (1/8)

## Slide 21
BSW
DCOM
COM
EM
All ECAN’s xml files must describe all messages and correct bits allocation and size (initial and range of values)
COM
Automation test (2/8)

## Slide 22
BSW
DCOM
COM
EM
ECAN will check all the MPC’s messages in Tx Messages except DIAG_PhysResp_MPC related to CAN transport
COM
Automation test (3/8)

## Slide 23
BSW
DCOM
COM
EM
Common function: ECAN_common_func.can
ECAN will check all the MPC’s messages in Tx Messages except DIAG_PhysResp_MPC which was related to CAN transport
COM
The value usually 0x7DF
Automation test (4/8)

## Slide 24
BSW
DCOM
COM
EM
Alive counter function: ECAN_chk_alive.can
Adding messages which includes alive counter inside.
COM
In this example, NMCSMlnd don’t have alive counter.
Ways to check:
1. Check inside messages
2. Check layout
3. Check Maximum values:
Checksum (0-255)
Alive counter 2bit (0-3) 3bit (0-7)
Automation test (5/8)

## Slide 25
BSW
DCOM
COM
EM
Checksum function: ECAN_chk_crc.can
Adding “Msg_” before messages which includes checksum inside.
COM
Modifying Messages based on format and correcting “databytes” using layout.
*NOTE: crcReceived: get from system
crcCalc: using formula to calculate.
Using masking for alive counter (BZ)
Automation test (6/8)

## Slide 26
BSW
DCOM
COM
EM
Initial value function: ECAN_chk_initval.can
Modify the main note. Addition length = MPC’s + 4
For this instance, it is CSM and addition length is 7
COM
2. Modifying Messages ID full message except DIAG_
Automation test (7/8)

## Slide 27
BSW
DCOM
COM
EM
COM
Download test scripts in tag “Testnote” (Coresi):
Step 1: Due to many components, define a common format add it to Test Environment. E.g: TC_gen.xml for chk_alivecnt
Step 2: Select “Configuration”
Step 3: In components tag, add *.can file include files: <Test_case>.can, <Common>.can, osek_tp.dll (C:\Program Files\Vector CANoe 10.0\Exec32\osek_tp.dll)
Step 4: Start coresi then select test cases, kick start button then check the results.
Step 5: Click start button “|>” then check the results.
Step 6: Open the Test Report.
1
2
3
4
5
Automation test (8/8)

## Slide 28
BSW
DCOM
COM
EM
COM
Manual test cases
– Need to modify TestSteps, Test response, Teststep keywords
Baudrate – Scan Baudrate
1: Public CAN
2: Private CAN
0x225 ID of message
Result:

## Slide 29
BSW
DCOM
COM
EM
COM
Manual test cases
Sampling point: Need CAN Stress or CAN Disturbance
1: Public CAN
2: Private CAN
0x225 ID of message

## Slide 30
BSW
DCOM
COM
EM
COM
Manual test cases
Set up Oscilloscope:
Type: Bus
Source Bus: B1 (CAN)
Trigger On: Start of Frame
Power signal:
Yellow: CAN high
Green: CAN low
Procedure:
Connect Hardware
Setup Oscilloscope
Shut the power down then turn it on
Press “RUN/STOP” to “RUN/STOP”
Adjust the start point of power and signal
Check the Δtime then compare to requirement
Start up time

## Slide 31
BSW
DCOM
COM
EM
COM
Sending only Public CAN Messages defined in the dbc
Undefined bits of send data shall be sent as 0 (1/2)
1st Method: Open the message layout then check the un-used (reserved) bits are 0 or 1
Manual test cases

## Slide 32
BSW
DCOM
COM
EM
COM
2nd Method: checking log files
Step 1: Setup Logging, select the message need to be filtered
Step 2: Chose the stored folder, record then check the log files.
Sending only Public CAN Messages defined in the dbc
Undefined bits of send data shall be sent as 0 (1/2)
Manual test cases

## Slide 33
BSW
DCOM
COM
EM
COM
Manual test cases
Check public CAN Tx messages priority
Step 1: Filter all public CAN Tx messages
Step 2: Start then logging record
Step 3: Reset CAN “1101”
Step 4: Check the first message (ID) sent after error frame (which was created by resetting) is end
Working Voltage (8V - 18V with -/+0.3V tolerance)
Step 1: Filter all public CAN Tx messages
Step 2: Start then logging record
Step 3: Reset CAN “1101”
Step 4: Check the first message (ID) sent after error frame (which was created by resetting) is end

## Slide 34
BSW
DCOM
COM
EM
COM
Enable XCP communication over Extended CAN
1. Add frame from database move it to trace window then Tester present ON - Change to Extended session with service 0x10 03
3. Check DTO is disable then try to enable it using message “2E 05 30 80”
2. Tester present ON - Change to Extended session with service 0x10 03
62 05 30 00 Disable
62 05 30 80 Enable
Service 22 read
Service 2E write
Manual test cases

## Slide 35
BSW
DCOM
COM
EM
COM
Disable XCP communication over Extended CAN
1. Change the sent data
2. Check DTO is enable then try to disable it using message “2E 05 30 00”
When disable mode when changing sent data, DTO won’t receive messages.
62 05 30 00 Disable
62 05 30 80 Enable
Service 22 read
Service 2E write
Manual test cases

## Slide 36
BSW
DCOM
COM
EM
COM
Data Frame(Standard and Extended Frame) - (Diagnostic Trouble Code)
1. Change the type to “CAN Extended” save the dbc, restart the coresi then check DTCs (Clear and Read DTCs)
Format of Read DTCs contain Failure
<0x59> <02 4B> <E8 00 87> <0B>
<Service> <Subfunc> <DTC> <status>
Passive state - can be cleared
e.g: 0A = 1010 passive state (last bit =0)
Active state – failure communication
e.g: 0B = 1011 active state (last bit =1)
2. Check the feedback status is active state with extended frames’ messages –take picture for report
Manual test cases

## Slide 37
BSW
DCOM
COM
EM
COM
Remote Frame (Consists of all the fields except data field; RTR bit is recessive)
1. In CAN IG change add message then select CAN Remote Type then setting logging for record
Manual test cases
Press the keyword set in manual e.g: “z”
2. Open log file then check whether the remote message (no data fields) sent correctly or not.

## Slide 38
BSW
DCOM
COM
EM
COM
No Acknowlegement
In “Hardware” tag select “Network Hardware” then chose the “ACK Off” in CAN 1 (public)
Manual test cases
2. Check the signal, Data should show the error (Not Acknowlegement)

## Slide 39
BSW
DCOM
COM
EM
COM
Reset ECU
1101
Result
SOME ISSUES AND SOLUTIONS

## Slide 40
BSW
DCOM
COM
EM
COM
Wrong initial values
Reset then re-execute these cases if the initial values were wrong, you should confirm these values with the developers.
SOME ISSUES AND SOLUTIONS

## Slide 41
BSW
DCOM
COM
EM
COM
SFCAN VID case (last case) failed:
Please check the whether you are using *VID_Status2.can and testWaitForTimeout get signal
Please refer VID cycle time in DBC file for more detail.
Result
SOME ISSUES AND SOLUTIONS

## Slide 42: EM
BSW
DCOM
COM
EM
Error Management Test
QUALIFICATION AND HEALING TIME TEST
BASIC TEST
Create an error, corresponding DTC will be reported
Remove error, DTC will become history DTC
Create an error, DTC will be reported after qualification time
Remove error, DTC will become history DTC after healing time
DTC Types
Loss Communication
Alive counter error
Checksum error - CRC
Signal
invalid
Data length error - DLC

## Slide 43: EM
BSW
DCOM
COM
EM
FOCUS

## Slide 44: LOSS COMMUNICATION
EM
TO
CRC
BZ
DLC
INVALID VAL
RX NODE
TX NODE
TX NODE
TX NODE
TX NODE
TX NODE
TX NODE
2
1
1
2
2
2
1
2
Loss communication
Normally communication
CAN Protocol

## Slide 45: CHECKSUM
TO
CRC
BZ
DLC
INVALID VAL
EM
In order to warrant QUALITY of data field of some essential messages, customer defined a
CRC Sequence in DATA FIELD of those ones.
CRC Sequence
0 – 8 bits
TX NODE
RX NODE
Data frame
CRC Sequence is calculatored before data frame transmited
CRC Sequence is calculatored after data frame receivered
Equal ?
Data and security correct
Yes
No
Reported CRC fault
64 bits Data field

## Slide 46: ALIVE COUNTER
Alive counter data
The data length is based on specific message.
CRC
BZ
DLC
INVALID VAL
TO
EM
TX NODE
RX NODE
Data frame
When a message is transmitted successfully
When a message is received successfully
Equal ?
BZ is correct
Yes
No
Reported BZ fault
txCnt++ txCnt<16
rxCnt++
rxCnt<16
In order to warrant SECURITY of data field of some essential messages, customer defined a ROLLING COUNTER SIGNAL in DATA FIELD of those ones.

## Slide 47: DATA LENGTH CODE
CRC
BZ
DLC
INVALID VAL
TO
EM
Message frame
The data length is maximum 8 bytes.
TX NODE
RX NODE
Data frame
Initial: 8 bytes data
Miss 1 byte LSB
Equal ?
DLC is correct
Yes
No
Reported DLC fault
Coresi is simulated to transmit 7 bytes data

## Slide 48: INVALID VALUE
DATA FIELD
0 – 8 bytes (MSB --- LSB)
TX NODE
RX NODE
Data frame
SOFTWARE
Signal Values are defined
in of Range
Data value is set in data frame
In of range ?
Signal value is correct
Reported invalid value fault
COMPARE
Yes
No
CRC
BZ
DLC
INVALID VAL
TO
EM
Using the coresi to config signal value

## Slide 49: CORESI RESTBUS
HOME
CORESI
Step 1
WHAT WE NEED BEFORE START ?
GEN - TOOL
CORESI
Gen-tool
Gen-tool\dbc
Gen-tool\source
Source\coresi
Source\generate
.dbc file
pubc_cola
Coresi
Vs_HMAC_VF00
Step 2
Step 3
Step 4
Step 5
Step 6
Step 7
Step 8
Step 9

## Slide 50: CORESI RESTBUS
Step 1: Open Gen-tool\dbc forder, copy file .dbc to this forder, open this file, right-click to MPC , export to file .xml, and save file .xml in the same location of .dbc
HOME
Step 1
Step 2
Step 3
Step 4
Step 5
Step 6
Step 7
Step 8
Step 9
CORESI

## Slide 51: CORESI RESTBUS
Step 2: Choose Signals, then choose File\Export\Export List of Objects and save file .csv in the same location of file .xml
HOME
Step 1
Step 2
Step 3
Step 4
Step 5
Step 6
Step 7
Step 8
Step 9
CORESI

## Slide 52: CORESI RESTBUS
Step 2: Choose Signals, then choose File\Export\Export List of Objects and save file .csv in the same location of file .xml . After that, edit .csv file as below:
Open .csv file, you can see it’s so difficult to follow. You must change its format. So, firtly you need choose all contents and Ctrl+C
Then you must Ctrl+V to copy all contents to nodepad++. You can see digit {“}. So, you must delete all {“}, replace by ‘space’ , Ctrl+A to choose all contents and Ctrl+C.
Then you overwrite this contents to .csv file by Ctrl+V. You can see it’s so easily to follow.
HOME
Step 1
Step 3
Step 4
Step 5
Step 6
Step 7
Step 8
Step 9
CORESI
Step 2

## Slide 53: CORESI RESTBUS
Step 3: We need modify contents in source forder. I will show you what’re contents need to modified?
3.1. Open location source\coresi_geely\coresi_geely_pubcan\pubc_coresi_geely_cola and
source\generator_cola , you need modify highlighted file as below:
.cola file
Checksum
Counter
CRC function
.ini file
Location of .xml file
.lis file
Main Node names
.bat file
Location of python application file
Modification overview
HOME
Step 1
Step 2
Step 3
Step 4
Step 5
Step 6
Step 7
Step 8
Step 9
CORESI

## Slide 54: CORESI RESTBUS
Step 3: We need modify contents in source forder. I will show you what’re contents need to modified?
3.2. You need fix two .lis files firstly. How you know the main node is what? You can search it as below:
Open .dbc and check all message one by one
Node have this messages is main Node
MPC
Modify to:
HOME
Step 1
Step 2
Step 4
Step 5
Step 6
Step 7
Step 8
Step 9
CORESI
Step 3
1
2
3

## Slide 55: CORESI RESTBUS
Step 3: We need modify contents in source forder. I will show you what’re contents need to modified?
3.3. Next, you need fix two .ini files. You must copy .xml name and replace to busfile link in .ini files
HOME
Step 1
Step 2
Step 4
Step 5
Step 6
Step 7
Step 8
Step 9
CORESI
Step 3

## Slide 56: CORESI RESTBUS
Step 3: We need modify contents in source forder. I will show you what’re contents need to modified?
3.4. Next, you need fix two .bat files.
Check version of Python
Run OK ?
Next step
Replace by python link in C:\ismPython\V3_3_2 or the others base on your computer
Yes
No
HOME
Step 1
Step 2
Step 4
Step 5
Step 6
Step 7
Step 8
Step 9
CORESI
Step 3

## Slide 57: CORESI RESTBUS
Step 3: We need modify contents in source forder. I will show you what’re contents need to modified?
3.5. And then, you need fix all .cola files (6 files).
- (1) We will focus to find messages which contain checksum and counter. So, How we do it? We open .csv file , filter by name the “name” column, check by keyword “checksum or counter or similar words such as crc, chksum, cnt, alivecnt, alivecounter,….” . Example, I check messages which contain checksum, you do with “counter” similarly.
*Note: Checksum # CheckSum
.*?Checksum$|.*?CheckSum$|Checksum.*?|.*?Checksum.*?
.*?Checksum.*?
Checksum.*?
.*?Checksum$
.*?CheckSum$
‘Or logic’ all components together
Create new script and write be like it.
Another tip check quickly checksum and counter signals
HOME
Step 1
Step 2
Step 4
Step 5
Step 6
Step 7
Step 8
Step 9
CORESI
Step 3

## Slide 58: CORESI RESTBUS
Step 3: We need modify contents in source forder. I will show you what’re contents need to modified?
3.5. And then, you need fix all .cola files (6 files).
- (2) Next, we will focus to overwrite new checksum counter strings. So, firstly we need Ctrl+F to search “WHERE name” location, we will see the old checksum counter strings. After that, we copy the new one which’re created in previous slide(page 26) and replace its to suitable location. Example, I will modify the file below:
We can see:
1 location contains checksum
3 locations contain alive counter
8 locations contain both checksum and counter
New strings
*Note: - ‘?!’ means ‘NOT’, attend it.
- Check again after modify
HOME
Step 1
Step 2
Step 4
Step 5
Step 6
Step 7
Step 8
Step 9
CORESI
Step 3

## Slide 59: CORESI RESTBUS
Step 3: We need modify contents in source forder. I will show you what’re contents need to modified?
3.5. And then, you need fix all .cola files (6 files).
- (3) We will focus to change the checksum functions, the counter functions and formula calculators crc in file source\coresi_geely\coresi_geely_pubcan\pubc_coresi_geely_cola\capl_code_cangen_geely.cola. To do it, we base on developer requirements and previous released coresi.
Checksum func ()
Calculator crc func()
Counter func ()
HOME
Step 1
Step 2
Step 4
Step 5
Step 6
Step 7
Step 8
Step 9
CORESI
Step 3

## Slide 60: CORESI RESTBUS
Step 4: Run the .bat file to generate to 3 forder: databases, models and panels in the same location with pubc_coresi_geely_cola forder.
See this report ?
Errors
Next step
Yes
No
Want to fix
Click here
HOME
Step 1
Step 2
Step 3
Step 4
Step 5
Step 6
Step 7
Step 8
Step 9
CORESI

## Slide 61: CORESI RESTBUS
Step 5: Using Beyond Compare 4 to compare genterated forders and similary forders in coresi forder one by one.
Generated forders
Coresi forders
[want to updated]
Copy essential contents from generated forders to similary coresi forders, delete inessential files in coresi forder based on .dbc file
* Note: - Confidently copy all panels to coresi.
- Attend to available in checksum counter function and formula calculator crc old coresi version. It’s based on requirements and developer.
HOME
Step 1
Step 2
Step 3
Step 4
Step 5
Step 6
Step 7
Step 8
Step 9
CORESI

## Slide 62: CORESI RESTBUS
Step 6: Configure coresi [.cfg file] . Open .cfg file in coresi forder and do next steps as below:
6.1. Add nessesary databases
Make sure these 6 databases are available
Add this database from coresi forders with location : sandbox\vs_HMAC_VF00\vs_VF00_databases
Add this database from coresi forders with location : sandbox\vs_HMAC_VF00\vs_VF00_gen_databases
HOME
Step 1
Step 2
Step 3
Step 4
Step 5
Step 6
Step 7
Step 8
Step 9
CORESI

## Slide 63: CORESI RESTBUS
Step 6: Configure coresi [.cfg file] . Open .cfg file in coresi forder and do next steps as below:
6.2. Add/remove suitable Network Nodes and configure
Make sure all essential Nodes are added
Base on .dbc file and vs_VF00_gen_models forder
Compile all Network Nodes to check error.
1
2
3
HOME
Step 1
Step 2
Step 3
Step 4
Step 5
Step 7
Step 8
Step 9
CORESI
Step 6

## Slide 64: CORESI RESTBUS
Step 6: Configure coresi [.cfg file] . Open .cfg file in coresi forder and do next steps as below:
6.3. Check the checksum’s byte of all messages.
Matching together
1
2
3
4
5
The same name
HOME
Step 1
Step 2
Step 3
Step 4
Step 5
Step 7
Step 8
Step 9
CORESI
Step 6

## Slide 65: CORESI RESTBUS
Step 6: Configure coresi [.cfg file] . Open .cfg file in coresi forder and do next steps as below:
6.4. Build panels for coresi. We base on vs_VF00_gen_panels forder
Choose Signals tab
Base on panel forder to create all panel frames
Choose a panel
Choose to add link for this panel
Add suitable
link
Right-click on here
1
2
3
4
5
6
7
HOME
Step 1
Step 2
Step 3
Step 4
Step 5
Step 7
Step 8
Step 9
CORESI
Step 6

## Slide 66: CORESI RESTBUS
Step 6: Configure coresi [.cfg file] . Open .cfg file in coresi forder and do next steps as below:
6.5. Pre-test all panels. Example, I will pre-test “bcm_cs_icm_0” panel as below:
Choose Signals tab
Choose panel
Compare all message names one by one
Same ?
Error
Complete
Want to fix
Click here
No
Yes
1
2
3
HOME
Step 1
Step 2
Step 3
Step 4
Step 5
Step 7
Step 8
Step 9
CORESI
Step 6

## Slide 67: CORESI RESTBUS
Step 7: Cleaning and packing coresi forder after testing in lab
- We must delete all .cbf, .ini, .stcfg file in updated coresi forder.
- We must save .cfg file with version Canoe8.2
- Changing subforder names of coresi forder base on Project name, and changing codes if It’s directly related to subforder names.
HMAC_VF00_V1.0_RC01
Project name
HOME
Step 1
Step 2
Step 3
Step 4
Step 5
Step 6
Step 7
Step 8
Step 9
CORESI

## Slide 68: CORESI RESTBUS
Step 8: Testing in Lab
HOME
Step 1
Step 2
Step 3
Step 4
Step 5
Step 6
Step 7
Step 8
Step 9
CORESI

## Slide 69: CORESI RESTBUS
Step 9: Checkpoint on MKS
HOME
Step 1
Step 2
Step 3
Step 4
Step 5
Step 6
Step 7
Step 8
Step 9
CORESI

## Slide 70: CORESI RESTBUS
SOME ISSUES AND SOLUTIONS
HOME
Step 1
Step 2
Step 3
Step 4
Step 5
Step 6
Step 7
Step 8
Step 9
CORESI
Step 4: You can’t generate to 3 forders: database, model, and panel
Solutions: Make sure all forder and sub-forder names in locations don’t have space. Sometime .dbc file contains special symbol, so you must check again .dbc file and confirm with your developer. After .dbc file is modified, you need generate .xml file again and save by previous name. Make sure .xml file name in .ini file is right. Make sure main node name in .lis file is right.

## Slide 71: CORESI RESTBUS
SOME ISSUES AND SOLUTIONS
HOME
Step 1
Step 2
Step 3
Step 4
Step 5
Step 6
Step 7
Step 8
Step 9
CORESI
Step 6: Panel Error
Solutions: Firstly, you need check link of panel [.xvp file]. You need check again step 3.5.1. You need check pubc_env_autogenerate database file , if it has messages similar “alivecounter_Rv” (Raw value), you must generate again by current gen-tool or another gen-tool and restart at step 3.

## Slide 72
Frame Formats
Standard Frame - 11bit Identifier
Extended Frame - 29 bit Identifier
Frame Types
Data Frame
Remote Frame
Error Frame
Overload Frame
Inter-frame Spacing
CAN Protocol
HOME
CAN message
Appendix

## Slide 73
Standard Data Frame Format
Control Field
SOF
RTR
11 Bit Identifier
Arbitration Field
Data Field
CRC Field
DLC (4)
IDE
r0
Field
ACK
End of Frame
Extended Data Frame Format
SOF
SRR
11 Bit Identifier
Arbitration Field
18 Bit Identifier
Control Field
RTR
Data Field
DLC (4)
IDE
r1
r0
0 to 64 Bits
0 to 64 Bits
15 Bits
7 Bits
Inter-
mission
Difference between Standard Frame and Extended Frame
Differs only in Arbitration field and Control field
3 Bits
Bus Idle
Bus Idle
Ack Slot
CRC Delimiter
Ack Delimiter
CAN Protocol
HOME
CAN message
Appendix

## Slide 74
Remote Frame Format
Control Field
SOF
RTR
11 Bit Identifier
Arbitration Field
CRC Field
DLC (4)
IDE
r0
Field
ACK
End of Frame
15 Bits
7 Bits
Inter-
mission
3 Bits
Node acting as Receiver for certain data initiates a Remote frame
Consists of all the fields except data field as compared to a data frame
Contrary to Data Frames, the RTR bit is recessive
Exists for both the standard and extended format
Ack Slot
CRC Delimiter
Ack Delimiter
CAN Protocol
HOME
CAN message
Appendix

## Slide 75
Error Frame Format (Active Error Frame)
Error Frame
Frame
Uncompleted
Inter-
mission
6 Bits
0 -6 Bits
8 Bits
Error Delimiter
Superposition of
Error Flag
Error Condition
3 Bits
Error flag can be transmitted by both Transmitter and Receiver node
Error flag can start within the frame that is currently being transmitted
Types of Error flags
Active Error flag - consists of 6 consecutive ‘dominant’ bit sent by Error Active node
Passive Error flag - consists of 6 consecutive ‘recessive’ bit sent by Error passive node
CAN Protocol
HOME
CAN message
Appendix